## Slide 1: Object Detection Inference on PYNQ-Z2
電子碩一 范詠為
資工碩一 吳泓毅
電子碩一 林子軒

## Slide 2: Outline
YOLOv1 Intro
System Flow
Dataset
Implementation & Encountered Problem
  model architecture & experiment
  non maximum suppression
  vivado ip flow (stitich model IP & nms IP)
  host program
Conclusion
Reference

## Slide 3: Object Detection – YOLOv1
An one-stage frameworks for object detection task

## Slide 4: System Flow (on PYNQ-Z2)
image blending
NN model
NMS
image preprocessing
3xHxW
3x48x48
SxSx(5B+C)
class,score,x,y,h,w
3xHxW
PS
PL

## Slide 5: Dataset
PASCAL Visual Object Classes (VOC):
  year 2007
  20 classes.
  2501 images
Using training set to train and validation:
  YOLOv1 needs pretrained weights to prevent overfitting, but due to time restriction, we didn’t pretrained on other dataset like COCO or ImageNet on our model to get pretrained weights and do transfer learning on VOC dataset.

## Slide 6: Model Architecture
Image size is 448x448
24 Conv Layer + 2 fully connected Layer
The last layer need 4096x(7x7x30) = 6021120 parameters

## Slide 7: Model Compression
Change image size from 448x448 to 48x48 for lower inference time
Change 24 Conv Layer + 2 fully connected Layer to 4 Conv Layer and 1 fully connected Layer
Shrink dimension of last layer from 7x7x30 to 3x3x30, now it needs (3x3x32)x(3x3x30) = 77760 parameters, which is much smaller than 6021120 parameters
5 (box coordinate and confidence score)
z
20(class confidence score)
5 (box coordinate and confidence score)
If we remove one box, number of parameters change from 7x7x30 to 7x7x(30-5)=1225
If we shrink grid size to 3x3, number of parameters change from 7x7x30 to 3x3x30=270

## Slide 8: Model Architecture
48x48x3
Conv + MaxPool
Conv + MaxPool
24x24x64
12x12x64
6x6x64
3x3x32
Conv + MaxPool
Conv + MaxPool
Fully Connected
3x3x30
NMS

## Slide 9: Experiment
Model | mAP(PC side) | mAP(PYNQ-Z2 side)
3W3A | 50.9% | 37.7%
4W4A | 70.2% | 52.1%
5W5A(lower PE and SIMD) | 91.9% | 68.2%

## Slide 10: Problem encountered and Solved
Problem: Output of model is integer because of BNN, but it is expected to be small floating point.
Solved: When we transfer onnx to finn support layer, the last operation which let integer to be floating point will be removed. So we need to do postprocessing by ourselve to let model’s output value reasonable.
[-516,-3585,-5,-475…..]
output of model on FPGA
transfered by ourselves
after postprocessing
[0.0838, -0.5943,0.19677, 0.09283]

## Slide 11: Non Maximum Suppression (NMS)
select best bounding boxes out of many overlapping bounding boxes
  remove bbox with score < score_th
  sort by score from highest to lowest
  while bboxes list is not empty
    pop one bbox (B1), keep other bbox (B2) in list if
      B1 and B2’s predicted class are different
      B1 and B2’s predicted class are same and iou(B1, B2) < iou_th
    append B1 to final return list
bounding box (bbox)
(class, score, x, y, h, w)

## Slide 12: Non Maximum Suppression (NMS)
select best bounding boxes out of many overlapping bounding boxes
  remove bbox with score < score_th
  sort by score from highest to lowest
  while bboxes list is not empty
    pop one bbox (B1), for other bboxes (B2), keep B2 in list if
      B1 and B2’s predicted class are different
      B1 and B2’s predicted class are same and iou(B1, B2) < iou_th
    append B1 to final return list
bounding box (bbox)
(class, score, x, y, h, w)

## Slide 13: Non Maximum Suppression (NMS)
select best bounding boxes out of many overlapping bounding boxes
  remove bbox with score < score_th
  sort by score from highest to lowest
  while bboxes list is not empty
    pop one bbox (B1), for other bboxes (B2), keep in list if
      B1 and B2’s predicted class are different
      B1 and B2’s predicted class are same and iou(B1, B2) < iou_th
    append B1 to final return list
bounding box (bbox)
(class, score, x, y, h, w)
B1
B2

## Slide 14: Non Maximum Suppression (NMS)
C++ array implementation
nms.py
nms.cpp
remain_list
False | False | True | True | True
0.9 | 0.8 | 0.75 | 0.6 | 0.4
0 | 0 | 1 | 0 | 1
scores
class_preds
top
iou=0.9
iou=0.2

## Slide 15: NMS IP (nms.cpp)
read_input()
cellboxes_to_boxes()
non_max_suppression()
hls::stream<fixed>& inData
fixed predictions[S*S*(C+B*5)]

## Slide 16: NMS IP (nms.cpp)
read_input()
cellboxes_to_boxes()
non_max_suppression()
hls::stream<fixed>& inData
fixed predictions[S*S*(C+B*5)]
fixed bboxes[S*S*5]
unsigned class_preds[S*S]

## Slide 17: NMS IP (nms.cpp)
read_input()
cellboxes_to_boxes()
non_max_suppression()
hls::stream<fixed>& inData
fixed predictions[S*S*(C+B*5)]
fixed bboxes[S*S*5]
unsigned class_preds[S*S]
fixed nms_bboxes[S*S*5]
unsigned nms_class_preds[S*S]
unsigned nms_num

## Slide 18: NMS IP (nms.cpp)
read_input()
cellboxes_to_boxes()
non_max_suppression()
hls::stream<fixed>& inData
fixed nms_bboxes[S*S*5]
unsigned nms_class_preds[S*S]
unsigned nms_num

## Slide 19: NMS Encountered Problem
cannot use dataflow due to algorithm charcteristic
  use stream input then buffer values to perform nms algorithm
cannot synthesize to 10ns if using “float” datatype
  due to long latreny of floating point divider (iou = intersection / union)
  change datatype to ap_fixed<32, 4>

## Slide 20: Vivado IP Flow
Since we have NMS block after FINN model, we cannot directly use model’s bitstream
Instead, we get the generated model’s IP and connect it with NMS IP with Vivado tool
YOLO model
NMS
How to connect?

## Slide 21: Vivado IP Flow
We refer to “pynq_shell_project.png” in Lab FINN and found we need
  ZYNQ, finn_design_v1_0, Nms, DMA, Data Width Converter
YOLO model
NMS
DMA
DWC
DWC
finn_design_v1_0

## Slide 22: Vivado IP Flow
Our Final Block Diagram
DMA_in
DWC
4B
1B
DWC
2B
4B
finn
nms
axis
m-axi
buf

## Slide 23: Host Program
We modify FINN-generated driver.py & driver_base.py to adapt to our new design since it would be challenging to write from scratch

## Slide 24: Host Program
driver.py
change to

## Slide 25: Host Program
driver_base.py
design_1.hwh
xnms_hw.h

## Slide 26: Host Program Encountered Problem
The host program stuck on loading bitstream and we still cannot find a solution
  So we currently put nms to PS side…
Pynq board sometimes give “No Devices Found” error

## Slide 27: Current System Flow (on PYNQ-Z2)
image blending
NN model
NMS
image preprocessing
3xHxW
3x48x48
SxSx(5B+C)
class,score,x,y,h,w
3xHxW
PS
PL

## Slide 28: Conclusion
YOLOv1 needs pretrained weights to prevent overfitting, since we modify the model structure, we cannot directly load original pretrained weights, and we don’t have time to pretrain on large dataset like ImageNet, either.
We don’t familiar with how to stitch FINN model and other IPs together, so it is still a major problem to be solved.

## Slide 29: Reference
You Only Look Once: Unified, Real-Time Object Detection
LPYOLO: Low Precision YOLO for Face Detection on FPGA
Lightweight CNN Image Classifier with On-chip Preprocessing
Xilinx_QNN-MO-PYNQ_tiny-yolo-image
Fixed Point Implementation of Tiny-Yolo-v2 using OpenCL on FPGA